| Contribution: | NTCO313 |
| --- | --- |
| Date: | May 18, 2005 |
| Working Group: | Network Working Group |
| Title: | 9-1-1 proposals Questions |
| Issues Addressed: | Follow-on Questions on the two proposals on for a different method to deliver 9-1-1 service for calls made from mobile voice over internet protocol devices and to develop possible solutions to enable PSAPs to meet publicly expected service standards.. |
| Source: | Francois D. Menard Project Manager Xit telecom inc. 1350 Royale, Office 800 Trois-Rivieres, QC, G9A 4J4 Tel: (819) 374-2556 x 268 Fax: (819) 374-0395 Mobile: (819) 692-1383 @: fmenard@xittelecom.ca |  |
| Distribution: | NTWG Interested Parties |
| Reference: | ESWG TIF35 |
| File Name: |  |
| Notice: | This contribution has been prepared by Xit telecom to assist the Network Working Group as basis for discussion. This should not be construed as a binding proposal on Xit telecom. Specifically, Xit telecom reserves the right to amend, modify or withdraw this contribution at any time. |

# Background

- On April 15 2005, the two architecture proposals were submitted for review by NTWG.

Additional questions on ESCO0193

- How is the proposed architecture capable of supporting the following PSAP call control features:

    - Bureau-Hold;

    - Ringback calling party;

    - Howler tone.

- Can you elaborate on the requirement to removing the routing logic (ESN), restrictions on TN to location (FX service)?

- Would the nation wide LAN interconnecting the 9-1-1 Tandem Switches/Selective Routers provide to be a suitable backbone for implementing HPC for NPA 710?

Additional questions on ESCO0196:

- How is the proposed architecture capable of supporting the following PSAP call control features:

    - Bureau-Hold;

    - Ringback calling party;

    - Howler tone.

- Is SS7 interconnection necessary in the proposed architecture?

- Is Bell Canada intending on discarding Via fields as calls get routed through the B2BUA?

*** END OF DOCUMENT ****